## Slide 1: Predict the solar power using time series for various time windows
Renewable Energy Industry

## Slide 2: V
Slide 1
Problem Statement and Business Overview
Data Pre Processing and Feature Engineering
Model Building
Metric Evaluation & Patterns
Conclusion
AGENDA

## Slide 3: Over View
Objective
Company Statement
To ensure the efficient use of energy PV systems it becomes important to forecast information reliably. The accurate prediction of solar power variation can enhance the quality of service. This integration of solar energy and accurate prediction can help in better planning and distribution of energy.
The past records of a month data with various time windows are present and need to predict the solar power for various time windows.
Data has values for energy from a solar plant for the month of January 2018 (02-01-2018 to 31-01-2018).
Each day has time windows for 5 minutes, 10 minutes, 15minutes, 30 minutes and 60 minutes.

## Slide 4: Business Problem
The increasing demand for energy is one of the biggest reasons behind the integration of solar energy into the electric grids or networks.
To ensure the efficient use of energy PV systems it becomes important to forecast information reliably.
The accurate prediction of solar power variation can enhance the quality of service. This integration of solar energy and accurate prediction can help in better planning and distribution of energy.
Statistical Tools (Arima, STLF, ANN)
Solar Power data
Database to store data
Solar Plan power Prediction

## Slide 5: DATA PRE-PROCESSING
Data Pre-Processing
Dataset was been stored in the json file on various time windows into 5, 10, 15, 30 and 60 minutes.
This were extracted into 5 csv files with varying length.
The data was having some outliers at the end of each month were the power reading was very high when compared to the others.
The outliers were been replaced by near by value by just replacing the higher value with the preceding lower value.

## Slide 6: Outlier value in various time windows
The outliers might have been included due to improper recording or miss typing due to which the statistical model gets affected a lot.
There are 5 html files for every time window depicting the power at various times.
5 Minutes
10 Minutes
15 Minutes
30 Minutes
60 Minutes

## Slide 7: Demo graphs of the Final Data Frame
 | Total Observations | Total variables | Split Observations | Target Variable | Evaluation Metric
5 Minutes | 4620 | 2(Time and Target) | 3542-1078 | Units Produced | RMSE and MSE
10 Minutes | 2310 | 2(Time and Target) | 1771-539 | Units Produced | RMSE and MSE
15 Minutes | 1530 | 2(Time and Target) | 1173-357 | Units Produced | RMSE and MSE
30 Minutes | 750 | 2(Time and Target) | 575-175 | Units Produced | RMSE and MSE
60 Minutes | 360 | 2(Time and Target) | 276-84 | Units Produced | RMSE and MSE

## Slide 8: Model Building

## Slide 9: Model Building approach
Solar Power Database
MODEL
Arima, Stlf, ANN
Input
Input
Output
Units produced
Predictions
New Data
Time series Data
Date
Target Labels
Convert Into Csv Readable file
0.2
0.8
1.5
Date
Units produced
0.2
0.8
1.5

## Slide 10: Case 1: Using STLF Technique to Build the Model
If we want to predict the power for longer time horizon then we should go for higher time window zone when compared to others.
As the error in predicting the longer time zone is lesser when compared to lower time window.
Chart: MSE
| 5 Minutes | 10 Minutes | 15 Minutes | 30 Minutes | 60 Minutes
mse | 0.091883 | 0.085158 | 0.079076 | 0.0632 | 0.062143
Chart: RMSE
| 5 Minutes | 10 Minutes | 15 Minutes | 30 Minutes | 60 Minutes
rmse | 0.30312 | 0.29182 | 0.2812 | 0.2514 | 0.24928

## Slide 11: Various Time Frame
Chart: 6 hours Time Frame
| 5 Min | 10 Min | 15 Min | 30 Min | 60 Min
 | 0.379 | 0.39 | 0.34 | 0.367 | 0.24
Chart: 1 day Time Frame
| 5 Min | 10 Min | 15 Min | 30 Min | 60 Min
 | 0.42 | 0.41 | 0.38 | 0.398 | 0.2598
From this plots we can say that 30 minutes time window is not appropriate for predicting the various time frame windows.
As the window Changes predicting with 30 mins window will be costly when comparing to others.
Chart: 1 hour Time Frame
| 5 Min | 10 Min | 15 Min | 30 Min | 60 Min
rmse | 0.0577 | 0.0408 | 0 | 0.07 | 0
rmse | 0.0577 | 0.0408 | 0 | 0.07 | 0

## Slide 12: predictions

## Slide 13: Case 2: Using Arima Technique to build the model
Chart: 
| 5_Min | 10_Min | 15_Min | 30_Min | 60_Min
RMSE | 0.4 | 0.38 | 0.36 | 0.26 | 0.239
Chart: 
| 5_Min | 10_Min | 15_Min | 30_Min | 60_Min
MSE | 0.16 | 0.15 | 0.13 | 0.065 | 0.0575
If we want to predict the power for longer time horizon then we should go for higher time window zone when compared to others.
As the error in predicting the longer time zone is lesser when compared to lower time window.

## Slide 14: Various Time Frame
From this plots we can say that 30 minutes time window is not appropriate for predicting the various time frame windows.
As the window Changes predicting with 30 mins window will be costly when comparing to others.
Chart: 1 hour Time Frame
| 5 Min | 10 Min | 15 Min | 30 Min | 60 Min
rmse | 0.0577 | 0.0408 | 0 | 0.07 | 0
rmse | 0.0577 | 0.0408 | 0 | 0.07 | 0
Chart: 6 hours Time Frame
| 5 Min | 10 Min | 15 Min | 30 Min | 60 Min
 | 0.353 | 0.342 | 0.299 | 0.3856 | 0.251
Chart: 1 day Time Frame
| 5 Min | 10 Min | 15 Min | 30 Min | 60 Min
 | 0.458 | 0.426 | 0.387 | 0.422 | 0.27928

## Slide 15: predictions

## Slide 16: Case 3: Using NNET Technique to build the model
If we want to predict the power for longer time horizon then we should go for higher time window zone when compared to others.
As the error in predicting the longer time zone is lesser when compared to lower time window.
Chart: MSE
| 5_Min | 10_Min | 15_Min | 30_min | 60_Min
mse | 0.11 | 0.0578 | 0.0558 | 0.049 | 0.0362
Chart: RMSE
| 5_Min | 10_Min | 15_Min | 30_min | 60_Min
rmse | 0.3316 | 0.24 | 0.2364 | 0.222 | 0.1902

## Slide 17: Various Time Frame
From this plots we can say that 30 minutes time window is not appropriate for predicting the various time frame windows.
As the window Changes predicting with 30 mins window will be costly when comparing to others.
Chart: 1 hour Time Frame
| 5 Min | 10 Min | 15 Min | 30 Min | 60 Min
rmse | 0.0645 | 0.0577 | 0 | 0.1 | 0
rmse | 0.0645 | 0.0577 | 0 | 0.1 | 0
Chart: 6 hours Time Frame
| 5 Min | 10 Min | 15 Min | 30 Min | 60 Min
 | 0.39 | 0.28 | 0.32 | 0.1958 | 0.208
Chart: 1 day Time Frame
| 5 Min | 10 Min | 15 Min | 30 Min | 60 Min
 | 0.418 | 0.32 | 0.35 | 0.28 | 0.2569

## Slide 18: Tools and Hyper parameters used in the model
STLF Model: The baseline package which was been used is forecast and no such tuning been done just the seasonality has been taken into account.
Arima Model: The baseline package which was been used is forecast and no such tuning been done just the seasonality has been taken into account.
Nnet Model: The baseline package which was been used is forecast and no such tuning been done just the seasonality has been taken into account.
Packages used are: Forecast, Lubridate, Ggplot, dygraphs, xts, and Tidy verse.
Tools Used: R for forecasting and model building, Python for data frame frame extraction from the file.

## Slide 19
CONCLUSION
Chart: Model Comparison Based on RMSE
| 5_Min | 10_Min | 15_Min | 30_min | 60_Min
Nnet | 0.3316 | 0.24 | 0.2364 | 0.222 | 0.1902
Arima | 0.4 | 0.38 | 0.36 | 0.26 | 0.239
STLF | 0.30312 | 0.29182 | 0.2812 | 0.2514 | 0.24928
FINAL MODEL: Nnet
For Long run prediction with 60 Min time window we should use Nnet.

## Slide 20
Chart: 1 Hour Window Predictions
| 5 Min | 10 Min | 15 Min | 30 Min | 60 Min
Nnet | 0.0645 | 0.0577 | 0 | 0.1 | 0
Arima | 0.0577 | 0.0408 | 0 | 0.07 | 0
STLF | 0.0577 | 0.0408 | 0 | 0 | 0
Chart: 6 Hours Window Predictions
| 5 Min | 10 Min | 15 Min | 30 Min | 60 Min
Nnet | 0.39 | 0.28 | 0.32 | 0.1958 | 0.208
Arima | 0.353 | 0.342 | 0.299 | 0.3856 | 0.251
STLF | 0.379 | 0.39 | 0.34 | 0.367 | 0.24
Chart: 1 Day Window Predictions
| 5 Min | 10 Min | 15 Min | 30 Min | 60 Min
Nnet | 0.418 | 0.32 | 0.35 | 0.28 | 0.2569
Arima | 0.458 | 0.426 | 0.387 | 0.422 | 0.279
STLF | 0.42 | 0.41 | 0.38 | 0.398 | 0.2598
CONCLUSION
From the above data it is clear that time window 30 performance is not good when compared to others.
We should use Stlf for 1 Hour window prediction.
For 6 hours window we should go Arima as it is stable in all windows.
For more than 1 day we should go for Nnet as the error will be less.

## Slide 21: THANK You